LAB 6
First of all we divided the frequency of 100MHz to 1000Hz using following code..
process(clk)
begin
if(clk'event and clk='1') then
if(count<49999) then -- we counting the number of clock till 50000
count<=count+1;
khz<='0';	-- making Khz <=0 for 50000 clk clock
else
count<=(others=>'0');	-- after counting till 50000 we starting
Khz<='1';	-- the counting from 0 and making Khz
end if;	-- <=1
end if;
end process;

Now we have divided the clk into 1Hz using folloewing code==
process(clk)
begin
if(clk'event and clk='1')then	--we counting the number of clock till 5000000
if(count2<4999999)then
count2<=count2+1;
Hz<='0';	---- making Hz <=0 for 5000000 clk clock
else
count2<=(others=>'0');	-- after counting till 5000000 we starting
Hz<='1';	-- the counting from 0 and making Hz
end if;	--<=1
end if;

end process;

The we have made 16 counter using for 1KHz:

process(Khz)
begin
if(Khz'event and Khz='1')then
if(countKhz<15) then	--counting till 15 and
countKhz<= countKhz+1;
else
countKhz<=(others=>'0');	-- initiaitng again from 0
end if;
end if;
end process;

Now we have made up down counter;

process(Hz)
begin
if(Hz'event and Hz='1')then
if(x=0) then
 countHz<=countHz+1;
if(countHz=14)then	-- we making x=1 if the counter reach 14	--given x=0
x<=1;
end if;
else
countHz<=countHz-1;	-- now we do down counting till 0 and
-- make x=0 given that before it was 1
if(countHz=1)then
x<=0;
end if;
end if;
end if;
end process;

Now we make the condition that if b=1 then it counitng automatically with made duty cycle.
We have made the condition that for counter of Hz =1 then duty of 1KHz the duty cycle will of 1/16 and next counter ir will be 2/16 and cycle goes on till counter is equal to 15 and then it will down counting.
Now if b=0 then given 4 bit vetcor if it equals to 1 then we using the frequency of counter at 1 means 1/16 duty cycle, if given input is 2 then we use the frequency for counter at 2 means 2/16 duty cycle and that goes on for different input value.
For seven segment we use if else condtion that is b=1 the glow the seven segment for 1 and if b=2 then glow the led for b=2 and it goes on till b=15;